SLAM PROCEDURES

I. Launching the real-time mapping process

Use of a launch file « outside_D.launch » for camera or « outside_laser.launch » for lidar (every launch files are in the my_pcl_tutorial/launch/ folder)

What it contains :
-A static transform between D435i and T265 related to the positions of the T265 and D435i on the drone (will be unchanged)
-A frequency reducer node ( parameters topic_in number number topic_out)
Current number parameters : 0 20 (meaning that it is dropping 0 message out of 20 messages, so no reducing)
-Pre-process filters for which parameters can be changed if necessary (but they should be fine like they are)
-Octomap node (the mapping process)

Parameters by default : frame_id (value = «map »)
max_range for the sensors (3.5 for d435i and about 15 for lidar)
min and max altitude for points to be integrated to the map (-3 to +5m)

INPUTs :
The lidar has to publish a topic « scan » and the D435i has to publish a topic /D435/depth/color/points. If different, a remaping or a tiny change in the launch file at the beginning of it can adjust to the topics’ names.
OUTPUT :
Once the launch file is runned, a topic /octomap_point_cloud_centers (sensor_msgs/PointCloud2) is published and is the one we are interested in monitoring.
It is updated in real-time and can(should at certain time) be saved at any time by executing the command in the terminal :
rosrun pcl_ros pointcloud_to_pcd input:=/topic_name
which will save the map as a .pcd file with a name composed of a sequence of numbers (maybe related to the time tag of the incoming message).
Warning : this command is not a one-shot script, but it will saves as many .pcd files as incoming messages from the published topic. That’s why the command needs to be killed quickly.
Maybe there is a turn-around.. I already tried to save it somewhere specific and with a certain name but it crashed. I will look again at it.
Human visualization of the map :
Use of rviz and listening to the topic /occupied_cells_vis_array
However I have never tried to save this topic which is not a pointcloud for visualization on another computer.
However concerning the 3D map as a PointCloud2 and saved as a .pcd, a launch file can be runned to visualize the map as a white pointcloud (a bit difficult to read for human eye).
For that, use the launch file « read_pcd.launch »
That launch files contains a node that will publish any input .pcd file as a pointcloud topic that can be listened on rviz. That node can be repeated as many time as wanted in the launch files in order to visualize several pointclouds at the same time for comparison.
Parameters : input_file(string) frame_id(string)
Comment : The input_file is the full address of the file (ex : /home/folder/file.pcd)

Warnings : 1) The output_topic must be listened to before the execution of the launch file in order for the node to start publishing the output_topic.
2) Somehow, if the launch file is executed alone, the published output_topic will be published only once so if someone removes the topic from rviz and put it back, rviz will lose the pointcloud, and the operator will need to relaunch the launch file. I noticed that if a rosbag (of any kind) is executing in background, the topics will be published continuously and there is not this problem.

II. Post-Process the obtained 3D map : Improve the Quality.
A) Remove the aberrant data

Use of a service called « outliers_removal ».
It removes the outliers which represents aberrant data from a pointcloud. It takes in entry a .pcd and returns a .pcd file.

Parameters : file_in(string) file_out(string) radius_search(double) min_neighbors_in_radius(int)

Comment : The file_in and file_out are the full addresses of the files (ex : /home/folder/file.pcd)

Procedure :
Terminal 1
Command  :
rosrun my_pcl_tutorial conversion_extraction_server
Normal output :

Terminal 2
Command : rosrun my_pcl_tutorial conversion_extraction_client file_in file_out
Example : rosrun my_pcl_tutorial conversion_extraction_client /home/dcas/m.dreier/Documents/PCD_FILES/Test3/my_map.pcd /home/dcas/m.dreier/Documents/PCD_FILES/Test3/my_map_denoised.pcd
Normal Output on Terminal 2 :

Normal Ouput on Terminal 1 :
B) Denoise a 3D DEM map

Use of a service called « denoising ».
This services denoise a pointcloud and writes it as another .pcd file.

Parameters : file_in(string) file_out(string)

Comment : The file_in and file_out are the full addresses of the files (ex : /home/folder/file.pcd)

Procedure :
Terminal 1
Command  :
rosrun my_pcl_tutorial denoising_server
Normal output : [ INFO] [1617294837.388376893]: Ready to denoise a DEM map (Pointcloud .pcd type)

Terminal 2
Command : rosrun my_pcl_tutorial denoising client file_in file_out
Example : rosrun my_pcl_tutorial denoising_client /home/dcas/m.dreier/Documents/PCD_FILES/Test3/my_map.pcd /home/dcas/m.dreier/Documents/PCD_FILES/Test3/my_map_denoised.pcd
Normal Output on Terminal 2 : [ INFO] [1617294851.887617715]: The call of the service denoising was a success

Normal Ouput on Terminal 1 : [ INFO] [1617294841.881168534]: request: file_in=/home/dcas/m.dreier/Documents/PCD_FILES/Test3/my_map.pcd file_out=/home/dcas/m.dreier/Documents/PCD_FILES/Test3/my_map_denoised.pcd
[ INFO] [1617294851.884734933]: Sending back response: Denoising was a success
III. Generation of a 2D Occupancy grid from a 3D Dem map
A) Extraction of a 2.5D map from a pointcloud

Use of a launch file called « grid_map_pcl_loader_node.launch ».
From a 3D pointcloud (.pcd file) it extracts only one layer which contains the needed topographical information. It writes the output as a rosbag (.bag) file in the same folder as the input file.

Parameters :
-folder_path
-pcd_filename
-output_grid_map value=elevation_map.bag
-map_rosbag_topic value=grid_map
-map_layer_name value=elevation
-set_verbosity_to_debug value=false

Comment : Do not change the value of the following parameters map_rosbag_topic_value , map_layer_name, set_verbosity_to_debug.

B) Convertion of 2.5D rosbag map into a .pcd file

Use of a service called « conversion_extraction ».
It takes in entry the output rosbag of the «grid_map_pcl_loader_node.launch » and converts the data into a .pcd file.

Parameters : file_in(string) file_out(string)
Comment : The file_in and file_out are the full addresses of the files (ex : /home/folder/file.pcd)

Procedure :
Terminal 1
Command  :
rosrun my_pcl_tutorial conversion_extraction_server
Normal output :

Terminal 2
Command : rosrun my_pcl_tutorial conversion_extraction_client file_in file_out
Example : rosrun my_pcl_tutorial conversion_extraction_client /home/dcas/m.dreier/Documents/PCD_FILES/Test3/my_map.pcd /home/dcas/m.dreier/Documents/PCD_FILES/Test3/my_map_denoised.pcd
Normal Output on Terminal 2 :

Normal Ouput on Terminal 1 :

C) Generation of a 2D Occupancy Grid from an extracted pointcloud
Use of a service called « occupancymap_generator ».
This service generates an occupancy grid as 2 files, one which is an image .pgm file with black,white,grey space to visualize the grid map, and one .yaml which specifies the characteristics of the occupancy grid (resolution, width, height, origin coordinates). Such informations are also printed in the terminal when the service is called.
As a discretized version of the occupancy grid was wanted for the computation of the path-planning algorithm (existence of a path between two waypoints), a discretized version of the generated grid map is also generated. Only the wanted discretized resolution is asked in parameter, and a second grid map is generated from the first one. It will appear as two more files, one .pgm and one .yaml. The files will be generated at the same place of the file_output parameter except the name will contain the extension « _discretized ».

Parameters :
-string file_in (path and name of the file)
-string file_out (path and name of the file)
-string frame_id (frame id of the occupancy map)
-double resolution (in meter, of the occupancy grid)
-double resolution_discretized (in meter, of the discretized occupancy grid)
-double resolution_grid_map_pcl_node (in meter, resolution of the node grid_map_pcl_node)

Comment: Here, file_in must include the full address, including the « .pcd » of the input file. However, file_out must not contain the extension format of the file and should only include the path and the name of the wanted output. It is due to the fact 2 output files are generated for a single occupancy grid.
Example : file_in = /home/test/input.pcd file_out=/home/test/output
and the service will generate /home/test/output.pgm /home/test/output.yaml /home/test/output_discretized.pgm /home/test/output_discretized.yaml
Procedure :
Terminal 1
Command :
rosrun my_pcl_tutorial occupancymap_generator_server

Normal output :

Terminal 2
Command : rosrun my_pcl_tutorial occupancymap_generator file_in file_out frame_id resolution resolution_discretized resolution_grid_map_pcl_node
Example :

Full Procedure examples

1. Launch Mapping process (I)
2. Save map as a .pcd file (I)
3. Outliers removal on the .pcd file (II.A)
4. Denoise the .pcd file (II.B)
5. Use the Extraction service on the .pcd file (III.A)
6. Use the Conversion service on the rosbag (III.B)
7. Use occupancymap_generator service on the .pcd file (III.C)
However, some steps might be repeated in order to obtain better results.
For example, what I do and what gives nice results is :

1. Launch Mapping process (I)
2. Save map as a .pcd file (I)
3. Outliers removal on the .pcd file (II.A)
3.bis Outliers removal again (II.A)
4. Denoise the .pcd file (II.B)
5. Use the Extraction service on the .pcd file (III.A)
6. Use the Conversion service on the rosbag (III.B)
7. Denoise again the pcd (II.B)
8. Use occupancymap_generator service on the .pcd file (III.C)

We are free to try as many as we want different post-process procedures and play with the parameters of the different services and launch files. Indeed, The operating drone represents only the chapter I, which means that the material output (a .pcd file) from chapter I can be used several times and without constraints.